## Slide 1: Blur / Smooth Images – (7)
Understanding was the hard part!
In MATLAB, this is very easy!
First, we need to create the mask
  We do this by calling fspecial() mask = fspecial(‘average’, N);
  mask contains the averaging mask to use
  First parameter specifies we want an averaging mask
  N specifies the size of the mask  Bigger the N, more blurring we get

## Slide 2: Blur / Smooth Images – (8)
Next, call a command that will perform this multiply and sum command for each pixel in the image
  Use the imfilter() command
out = imfilter(im, mask);
  out: output image (this case  averaged output)
  im contains the image we want to blur
  mask: Convolution mask to use (this case  averaging)
Nice little note  imfilter() works on both
grayscale and colour images
  For colour, this automatically performs convolution on each channel individually and combines after

## Slide 3: Blur / Smooth Images – (9)
imfilter() performs image filtering using masks
  Essentially convolution
Filtering  Produce an output image that changes the frequency content of the image
  Blurring, Sharpening, Detecting Edges, etc.
Why are masks important?
  You change the size of the mask, and values in the mask and you get different results!
  Essentially how most filters in Adobe Photoshop and GIMP work

## Slide 4: Edge Detection – (5)
How do we do this in MATLAB?
  1) Create our Prewitt or Sobel Horizontal Masks: mask = fspecial(‘prewitt’); or mask = fspecial(‘sobel’);
  2) Get the Vertical Mask:
mask2 = mask’;  ‘ transposes a matrix
  3) Convolve with each mask separately
dX = imfilter(im, mask); dY = imfilter(im, mask2);
  4)Find the overall magnitude
mag = sqrt(double(dX).^(2) + double(dY).^(2));

## Slide 5: Edge Detection – (6)
Note: We must cast images to double for sqrt() func.
Now, we’ve found the overall gradient… how do we find an actual edge? Threshold the image
What do we mean by threshold?
  Values greater than a threshold is an edge (white)
  Values less than the threshold are not edges (black)
How do we detect edges in MATLAB? Very easy!
I = edge(im, ‘sobel’); or
I = edge(im, ‘prewitt’);
So, we can pretty much ignore the previous slide, but I put that in there so you can see where it comes from

## Slide 6: Edge Detection – (7)
You can also call the routines this way:
I = edge(im, ‘sobel’, thresh); or I = edge(im, ‘prewitt’, thresh);
  I specifies edges found in input (B & W image)
  im is the input image with edges to be found
  Second parameter specifies method of finding edges
  thresh determines threshold for finding edges
  If not specified, threshold will be found automatically
How do we use the thresh variable?
  Choose an intensity (e.g. 128)
  Any gradient value > 128 will be labeled white

## Slide 7: Edge Detection – (8)
Any gradient value < 128 is labelled black
thresh is between [0,1], so take your threshold and divide by 255 to use
i.e. I = edge(im, ‘prewitt’, 128/255);
Output image will give you a black and white image 
White is an edge, black is not an edge
  Only works for B & W images. To find edges for colour
images, convert the colour image to a B & W image
  Use gray = rgb2gray(im);
  rgb2gray converts a colour image into B & W by doing: I = (R + G + B) / 3  Each colour pixel is the average of the red, green and blue components

## Slide 8: Edge Detection – (9)
Sidenote: Here’s another way of finding the gradient
 Unsharp Masking
Probably heard this terminology in CSI? So what’s unsharp masking?
Let’s go back to Signals and Systems
  Suppose we perform a low-pass filtering of an image  Get a blurred version
  If we take the original image, and subtract its blurred version, what are we doing? Removing all low frequency components, so what’s left? High frequency!

## Slide 9: Edge Detection – (10)
High frequencies are essentially edge information
  Edges are sudden jumps  Essentially high frequency
How do we perform unsharp masking?
  1) Blur the image  Try using the following mask:
mask = fspecial(‘average’, 5); %5x5
  So… we blur! im_blur = imfilter(im,mask);
  2) Subtract the original image from the blurred
im_unsharp = im – im_blur;
Now, why are edges useful? We can use them to
sharpen images  Will take a look after this demo

## Slide 10: Image Sharpening – (2)
Use imfilter with unsharp masking
mask = fspecial(‘unsharp’);
The above syntax creates an unsharp mask in such a way where when you convolve, it will automatically subtract the image with a blurred version of itself and add the original image on top
Good for both x and y direction changes
How?
mask = fspecial(‘unsharp’); sharp = imfilter(im, mask);
This will perform the detection of abrupt changes, and adding them on top of the image all in one go.

## Slide 11: Segmentation via Thresholding
There are times when we want to separate objects (the things we want) from the background  Segmentation
To make this easier, we convert to a B & W image first if the image is in colour. Else just leave it alone
After conversion, most of the time the intensities of the objects are distinctly different from background
We can write code to save the pixels that match these intensities, and disregard the rest
Pixels that match  Set to white, else set to black
Output image will be binary  White belonging to object, and black belonging to background
 We can use this to mask out the background pixels

## Slide 12: Segmentation via Thresholding (2)
What do we do?
  Take a look at the histogram, and see which pixels are predominantly belonging to the object, and of the background
  We threshold the image using this information
  We then use this threshold map to figure out what pixels we want to keep, and what we want to disregard

## Slide 13: Topics Covered in this Presentation
 3rd Hour: 8:10 p.m. – 9:00 p.m.
Applications of Image Processing
Segmenting simple objects
Noise Filtering
Simple image stitching using template matching

## Slide 14: Noise Filtering
A common task in image processing is to eliminate or reduce image noise from an image
Image Noise: Pixels in an image that are corrupted undesirably
  Pixels could be corrupted in the acquisition process, or in transmitting, etc.
How do we reduce image noise?
  Think in the frequency domain  Noise is essentially high-frequency information
  If we blur the image, we would eliminate the noise, but the quality would reduce  blurring details

## Slide 15: Noise Filtering – (2)
We can generate artificial noise and add these to images
  Purpose is for research  Design good filters by recreating the noise we would encounter in practice
How do we generate artificial noise? Use imnoise
  We will be concerned with two ways of generating noise out = imnoise(im, ‘gaussian’, mean, var); out = imnoise(im, ‘salt & pepper’, prob);
First method generates Gaussian-based noise
  Usually encountered in transmitting process

## Slide 16: Noise Filtering – (3)
Second method generates “salt & pepper” based noise
  Also known as impulsive noise
  Called this way, because for monochromatic images, it literally looks like someone took salt (white pixels) and pepper (black pixels) and shook it over the image
  For colour images, specks of pure red, green and blue pixels appear
We can use blurring to get rid of Gaussian noise, but for impulsive noise, we need to use median filtering
  What’s median filtering? Like convolution, but we’re not doing a weighted sum

## Slide 17: Noise Filtering – (4)
For each pixel (r,c) in the image, extract an M x N subset of pixels centered at (r,c)
Sort these pixels in ascending order, and grab the
median value
 The output image at (r,c) is this value
How do we perform median filtering in MATLAB?
out = medfilt2(im, [M N]);

## Slide 18: Template Matching – (3)
Output is a correlation map
  To find the row and column co-ordinates of where the template best matches, do the following:
[row col] = find(C == max(C(:)));
So, how do we do image stitching?
  1) Extract a region in either image that is common between both  Template
  2) Find the co-ordinates of where this template is in both images
  3) Determine how much vertical and horizontal displacement there is between the two images

## Slide 19: Template Matching – (4)
4) Create an output image with dimensions that encapsulate both images together
5) Place one image on the left, then place the other image by displacing it over by the horizontal and vertical shift
 OK… let’s do some code!