## Slide 1: Computer Organization

## Slide 2
Computer organization and architecture involves many abstract concepts for the undergraduate beginner. Today, most students start undergraduate courses. In this way, they see the computer in a preconceived way, as a tool useful for tasks such as Internet browsing or text edition. This view bares few obvious relationships to Boolean algebra, logic gates, registers, or arithmetic logic units. There is then an enormous gap to fill in order to teach computer organization and architecture adequately. The gap is caused by the increasing number of abstraction layers interposed between the real hardware and end-user oriented applications. To close this gap, several teaching methods are currently being proposed. Most of them are based on extensive use of practical work to support lectures. Traditional approaches to introduce the study of computer organization and architecture, like the excellent one proposed by Patterson and Hennessy in [3], often limit practical work to using assembly language programming and associated assembler and simulation tools. This Section reviews modern approaches that aggregate effective hardware design and sometimes hardware implementation to help understanding computer architecture abstractions and to better motivate students to further work on the field. Originally, DRAMs had an asynchronous interface to the memory controller, so every transfer involved overhead to synchronize with the controller. The second major change was to add a clock signal to the DRAM interface, so that the repeated transfers would not bear that overhead. Synchronous DRAM (SDRAM) is the name of this optimization. SDRAMs typically also have a programmable register to hold the number of bytes requested, and hence can send many bytes over several cycles per request

## Slide 3
Computer organization and architecture involves many abstract concepts for the undergraduate beginner
Today, most students start undergraduate courses

## Slide 4
In this way, they see the computer in a preconceived way, as a tool useful for tasks such as Internet browsing or text edition.
This view impedes to see few obvious relationships to Boolean algebra, logic gates, registers, or arithmetic logic units.
There is an enormous gap to fill in order to teach computer organization and architecture adequately.

## Slide 5
To close this gap, several teaching methods are currently being proposed.
Traditional approaches to introduce the study of computer organization and architecture, like the excellent one proposed by Patterson and Hennessy in [3], often limit practical work to using assembly language programming and associated assembler and simulation tools.

## Slide 6
This Section reviews modern approaches that aggregate effective hardware design and sometimes hardware implementation to help understanding computer architecture abstractions and to better motivate students to further work on the field

## Slide 7
As Moore’s law continues to supply more transistors and as the processor– memory gap increases pressure on memory performance, the ideas of the previous section have made their way inside the DRAM chip. Generally, innovation has led to greater bandwidth, sometimes at the cost of greater latency. This subsection presents techniques that take advantage of the nature of DRAMs. As mentioned earlier, a DRAM access is divided into row access and column access. DRAMs must buffer a row of bits inside the DRAM for the column access, and this row is usually the square root of the DRAM size—for example, 2 Kb for a 4 Mb DRAM. As DRAMs grew, additional structure and several opportunities for increasing bandwidth were added. First, DRAMs added timing signals that allow repeated accesses to the row buffer without another row access time. Such a buffer comes naturally, as each array will buffer 1024 to 4096 bits for each access. Initially, separate column addresses had to be sent for each transfer with a delay after each new set of column addresses.

## Slide 8
As Moore’s law continues to supply more transistors and as the processor– memory gap increases pressure on memory performance, the ideas of the previous section have made their way inside the DRAM chip.
Generally, innovation has led to greater bandwidth, sometimes at the cost of greater latency.

## Slide 9
This subsection presents techniques that take advantage of the nature of DRAMs
As mentioned earlier, a DRAM access is divided into row access and column access.
DRAMs must buffer a row of bits inside the DRAM for the column access, and this row is usually the square root of the DRAM size—for example, 2 Kb for a 4 Mb DRAM.

## Slide 10
As DRAMs grew, additional structure and several opportunities for increasing bandwidth were added.
First, DRAMs added timing signals that allow repeated accesses to the row buffer without another row access time.

## Slide 11
Such a buffer comes naturally, as each array will buffer 1024 to 4096 bits for each access
Initially, separate column addresses had to be sent for each transfer with a delay after each new set of column addresses

## Slide 12
Originally, DRAMs had an asynchronous interface to the memory controller, so every transfer involved overhead to synchronize with the controller.
The second major change was to add a clock signal to the DRAM interface, so that the repeated transfers would not bear that overhead.

## Slide 13
Synchronous DRAM (SDRAM) is the name of this optimization.
SDRAMs typically also have a programmable register to hold the number of bytes requested, and hence can send many bytes over several cycles per request